## Slide 1: Lock Out Tag Out

## Slide 2: LOCK OUT / TAG OUT
THE ULTIMATE GOAL IS:
  To ensure the safety of employees by implementing policies and procedures to prevent, as necessary, the release of hazardous energy from power sources--or from a stored source in machines, equipment or processes.

## Slide 3: WHAT IS LOCKOUT/TAGOUT?
Lockout:
  The placement of a lock device on an energy-isolating device to ensure the equipment cannot be operated during equipment maintenance or repair
Tagout:
  The placement of a tag device on an energy-isolating device to warn of the danger of operating, and NOT to start the equipment until the tag is properly removed
    Note: Tagout can only be used where the employer can demonstrate the equivalent level of protection as Lockout

## Slide 4: Terms and Definitions
AFFECTED EMPLOYEE:
  One whose job requires them to operate/use or be in the area of machinery or equipment on which service/maintenance is being performed
AUTHORIZED EMPLOYEE:
  One who is qualified by training and experience to perform and is responsible for the lockout/tagout of machinery or equipment…

## Slide 5: TERMS AND DEFINITIONS Cont.
LOCKOUT DEVICE:
  A device such as a lock (key or combination) that holds/secures an energy-isolating device, thus preventing an energy source from operating
TAGOUT DEVICE:
  A prominent warning device, such as a tag with a means of attachment, which can be securely fastened to an energy-isolating device

## Slide 6: TERMS AND DEFINITIONS Cont.
CAPABLE OF BEING LOCKED OUT:
  An energy- isolating device (switch, lever, etc.) able to be locked out via a hasp or other means, to which a lock can be affixed
FULL EMPLOYEE PROTECTION:
  When a tagout device is used on an energy-isolating device which is able to be locked out, it MUST be attached at the SAME location as the LO device would be, AND demonstrate equivalent level of safety to the lockout program

## Slide 7: ENERGY CONTROL PROCEDURES
MUST BE WRITTEN AND INCLUDE:
  Scope
  Purpose
  Authorization

## Slide 8: ENERGY CONTROL PROCEDURES
MUST BE WRITTEN AND INCLUDE:
  Rules
  Techniques
  Enforcement

## Slide 9: ENERGY CONTROL PROCEDURES
Equipment specific procedures are required for each piece of equipment. One procedure is sufficient where multiple pieces of the exact same equipment are used.

## Slide 10: ENERGY CONTROL PROCEDURES Cont.
Stored energy sources, following the placement of lockout or tagout devices, shall be restrained, disconnected, relieved, and otherwise rendered safe

## Slide 11: HAZARDOUS ENERGY SOURCES
ENERGY SOURCES CAN BE:
  ELECTRICAL
  MECHANICAL
  PNEUMATIC
  HYDRAULIC

## Slide 12: Release from Lockout/Tagout
The work area shall be inspected to ensure that nonessential items have been removed and the equipment components are intact
The work area shall be checked to ensure that all employees have been safely positioned or removed

## Slide 13: Release from Lockout/Tagout Cont.
Lock out / Tag out devices shall be removed by the employee who placed the device, or under the direction of the employer, if the authorized employee is unavailable

## Slide 14: LOCKOUT/TAGOUT-HARDWARE
Lockout tagout devices shall be provided by the employer and must meet the minimum industry standard

## Slide 15: EQUIPMENT INSPECTIONS
The employer shall conduct an annual inspection and certify that the LO/TO policies and procedures are being complied with

## Slide 16: Training & Communication
The employer must provide training:
  To all employee’s on the current procedures
  Whenever LO/TO procedures are used
  Whenever there are changes in Job assignments, machinery/equipment, or processes that present any new hazards

## Slide 17: PROGRAM REQUIREMENTS
Your company should require contractors to have a Lock Out / Tag Out program that complies with the agency standards

## Slide 18: LOCKOUT/TAGOUT
IT’S A MATTER OF LIFE AND DEATH

## Slide 19: TEST
Name the four energy sources LO/TO addresses?
To use Tag Out instead of Lock Out, what must be demonstrated?
Who may remove a Lock Out device?

## Slide 20: TEST CONT.
Define “affected person” ?
After a Lock Out device is installed, what must take place?
Must employers conduct an inspection?

## Slide 21: QUESTIONS?